## Slide 1: Title Lorem Ipsum
Dolor Sit Amet
Consectetuer Elit
Nunc Viverra
Pellentesque Habitant
Lorem Ipsum

## Slide 2: Myo-Electric Hand: “Prosthetic Hand Replication Using EMG Based Approach”
Final Year BE Project Phase-2 Seminar

## Slide 3: CONTENTS:
INTRODUCTION
LITERATURE SURVEY
METHODOLOGY
SYSTEM IMPLEMENTATION
RESULTS,DISCUSSIONS
ADVANTAGES, DISADVANTAGES, APPLICATIONS.
CONCLUSION
FUTURE SCOPE

## Slide 4: SUB HEADINGS:
1.1 MOTIVATION
1.2 PROBLEM STATEMENT
1.3 OBJECTIVE
3.1 INTRODUCTION
3.2 BLOCK DIAGRAM
3.3 HARDWARE AND SOFTWARE

## Slide 5: 1.INTRODUCTION:
The human body contains many parts and out of these, hand is one of the vital part. Hand parts are very gentle and intricate structure.
This gives muscles and joints in the hand part a wide variety of actions and accuracy.
Having the ability to perform important essential actions symbolizes multiple degrees of freedom and is capable of performing integrated functions.
Joints provide the convenient freedom of movement and muscles serve to transfer rigid segments on each other.
The present developments in science and engineering technologies have led to the development of prosthetic hand based on muscle operated sensors.

## Slide 6: INTRODUCTION CONT. :
Prosthetics are non-natural devices designed to replace a missing body part, for example a leg or a hand.
The working principle of prosthetics is based on EMG signals. EMG is abbreviated as Electro Myo-Graph.
EMG signal is nothing but study of electrical signals in muscles.
The nervous system in our human body controls the contraction and relaxation activities of the muscles
This signal is a complex signal and is dependent on the anatomical and physiological properties of the muscle movements.
The EMG signal gets corrupted with noise as it encounters different tissues in the human body.

## Slide 7: 1.1 MOTIVATION :
Approximately 1 in every 200 people in India has undergone an amputation.
Annually, in India, approximately 156,000 people go through an amputation operation, and, there are currently over 1.7 million people in India with an amputated limb.
Amputations (because of trauma) have been declining over recent years, as have amputations from cancer.
Costs Of Arms range from 150K Rs to 360 K Rs depending on functionality and different features.
Artificial Organs need to be created to replace Human Organs
There Is no Cheap Alternative For Amputees

## Slide 8: MOTIVATION CONTD. :
When it comes to replacement of hands and legs there is no easy and cheap alternative to it.
Such people cannot perform functions which require using the hand, not even routine
activities in day to day life such as holding the objects, moving them, eating and other such similar functions.
Broadly speaking, these people are not self-sufficient, but they muscles in the remaining part of the arm which functions in a normal way
So we can extract EMG signals from the remaining part and can be used in limb replacing techniques.

## Slide 9: 1.2 PROBLEM STATEMENT:
People with physical disability are facing issues every day for living day to day life
Amputees face a Psychological Barrier when it comes to the looks and Aesthetics of the body
Amputees cannot overcome the hurdle of creating their Career as they had dreamed all their life
Researchers and scientists are working on brain signals controlled bionics hand but it is not 100% workable with everyone as it needs lot of practice for one to operate

## Slide 10: PROBLEM STATEMENT CONTD. :
It will be too Expensive for the middle class and poor people to afford.
Hand is one of the important parts in a human body and the people who are not having part of hand or whole hand by accident or by birth has lot of obstacles in doing their works.
There are plastic molded hands but it serves no help in doing the tasks.
Then we need to overcome the issues of weight , comfort.
Then we need to provide Accurate and Precise Prosthetics

## Slide 11: 2.Literature Survey:

## Slide 16: 3. METHODOLOGY: 3.1 INTRODUCTION:
The proposed system is based on the use of EMG signals to support the mechanism of the prosthesis.
For the aim of the project, the proposed system was established through two stages as follows.
A software that is responsible for extracting the EMG signal from the patient and analyze it to figure out the most suitable position on the stump of amputee to collect the signals, and a view of the planned GUI interface is illustrated in the below Figure.
Also, this software can help to train the patient how to control the three-dimensional hand in the program created using CAD.

## Slide 17
Connection Diagram:

## Slide 18: 3.2 BLOCK DIAGRAM:

## Slide 19: 3.3 HARDWARE AND SOFTWARE :
FIG ; Basic over view of Hardware Circuit blocks

## Slide 20
Fig; Differential amplifier
Fig; Band pass filter
Fig; Non inverting Amplifier

## Slide 21
Fig: Arduino Nano
Fig: Software IDE

## Slide 22
An EMG signal is an Electric Potential generated by Muscle Contraction.
It may be measured on the skin surface or by embedding sensors into deeper layers of the muscle.
Medical reference suggests that different compartments of the ear muscle related to hand and finger movement and EMG signal can still be measured from the forearm muscle even after the hand is amputated.
Therefore, theoretically, it is possible to use the EMG signal to control hand and ﬁnger movements.
Then the EMG signals need to be measured through the electrodes placed systematically

## Slide 23
Then the EMG signal needs to be filtered and pre processing needs to be done.
Then the processed signal needs to be input to a microcontroller.
Then the signals are used to control micro switches and the Servo Motors in the Artificial Arm.
Then the assembly in placed in a Container and placed on the arms of the User.
Then Succesive Iterations of Testing Is done and the Accuracy of the Grips Is Fine Tuned.

## Slide 24: 4.SYSTEM IMPLIMENTATION:
4.1 POWER SUPPLY
Two 9 volt batteries are both a convenient and safe way to power our EMG amplifier. Because we'll be attaching ourselves to the circuit, we don't want our circuit connected in any way to AC power from the wall.
The diagram below illustrates how to connect the batteries in a ±9 volt arrangement.

## Slide 25
4.2 – SIGNAL ACQUISITION
Next, we will work on the signal acquisition phase of your EMG circuit which we will use to measure our body’s nervous system’s electrical impulses used to activate muscle fibers.

## Slide 26
4.3 - SIGNAL CONDITIONING
In this phase, we’re going to take those very small signals measured in the SIGNAL ACQUISITION phase and amplify them.
First we will be inverting amplifier with a gain of -15. An inverting amplifier does exactly what it sounds like. It amplifies your signal but also inverts it.
Next, we are going to add a capacitor to AC couple the signal. AC coupling is useful in removing DC error offset in a signal.
Next we are going to add another inverting amplifier with a gain

## Slide 27
4.4 – CONNECTING THE ELECTRODES
For the bicep, the elbow is a suitable placement for ground.
The positive and negative electrodes should be placed on the upper arm as shown in the figure.
In my experience, the signal was stronger when electrodes were placed closer to the center of the body (medially) when the palm is facing upward.

## Slide 28
Smoothening

## Slide 29: 5. RESULTS AND DISCUSSIONS:
The EMG Signal was Acquired from the EMG Sensor
A EMG Signal Was fed into the Micro Controller which in turn perform the required necessary actions which is called Training
Then Serial Data from the Micro Controller is fed into the Simulating Software Called as Processing IDE
Then the minimum Threshold for reading the data is set.
Button Logic is used to train the Model
Tap and Hold Logic is used using Time as a Reference Value

## Slide 30
The Data is then Processed in the Processing IDE
The Prosthetic Hand then Mimics the actions of the Simulated Hand in IDE

## Slide 31: 6.1 ADVANTAGES
Easy To Use
Inexpensive
Affordable to the Masses
Light Weight
Accurate Grips
Repeatability and Mass Production is possible
Less Training is Required
Since Threshold is set few noise signals are also avoided

## Slide 32: 6.2 DISADVANTAGES
Takes time to Train
Many Small Tiny parts are required which are hard to assemble
Assembling is Difficult
Accuracy takes more time to Achieve
Precision needs to Fine Tuned

## Slide 33: 6.3 APPLICATIONS:
Prosthetic Hand acts as an Extension Of One’s Hand
People Who have lost A Part of their Arm can use this Prosthetic Hand
It can sometimes be used to reach places where a normal hand cant reach
It can be used in Environments where a regular Arm cant be used
It can be a substitute arm for Amputees

## Slide 34: 7. CONCLUSION
One of the main requirements of artificial arm is the functionality, since it should be as natural hand as possible.
In this study, a prototype of a prosthetic hand will be developed considering two movement opening and closing the hand and this will be the result of several designs.
More comprehensive study to cover a wider range of gestures can be considered in the future, for example, individual finger movements

## Slide 35: 8. FUTURE SCOPE:
Brain Signals in Addition Of EMG Signals can be used as inputs to power the upcoming prosthetic arms
A mini Solar Panel can be used as a Substitute Power Source
Electrodes Insertion can be made simpler and more Aesthetic

## Slide 36: THANK YOU